## Slide 1
DEPARTMENT OF INDUSTRIAL AND PRODUCTION ENGINEERING | BUET
Comparative Performance and Robustness Analysis of
Modified Vogel's and Modified Russell's Approximation Methods
under Interval Type-2 Trapezoidal Fuzzy Uncertainty
Md Sadiqul Haque (ID: 2008082) | Md Tanjil Haque (ID: 2008094)
Supervised by: Dr. Kais Bin Zaman, Professor, IPE, BUET
B.Sc. in Industrial & Production Engineering | June 2026
BUET — Bangladesh University of Engineering and Technology

## Slide 2
Presentation Outline
01
Transportation Problem Background
02
Uncertainty Modeling: T1 vs IT2 Fuzzy Sets
03
Research Gap & Problem Statement
04
Research Objectives & Scope
05
IT2 Fuzzy Framework: Fuzzification
06
IT2 Fuzzy Framework: KM & Defuzzification
07
Balance-Preserving Normalization
08
MVAM: Modified Vogel's Approx. Method
09
MRAM: Modified Russell's Approx. Method
10
MODI Optimization & Performance Metrics
11
Structural Regimes: Penalty-Sharp vs Diffuse
12
Synthetic Dataset Design
13
Results: Small & Medium Scale
14
Results: Large & Extended Scale
15
Statistical Benchmarking Summary
16
Problem Structure vs Problem Size
17
Cost Sensitivity Analysis
18
Footprint of Uncertainty (FOU) Sensitivity
19
Joint Robustness Assessment
20
Contributions, Limitations & Future Work
1 / 20

## Slide 3
The Transportation Problem (TP) — Background
Introduced by Hitchcock [1] (1941) & Koopmans [2] (1947)
Minimize total shipping cost from m sources → n destinations
Decision variable: x_ij = units shipped from source i to destination j
Subject to: supply & demand constraints + non-negativity
Objective Function:
Minimize Z = Σᵢ Σⱼ cᵢⱼ · xᵢⱼ
cᵢⱼ = unit cost (i→j) | xᵢⱼ = units shipped | Σᵢ sᵢ = Σⱼ dⱼ (balance)
[ Figure: Supply-Demand Network Diagram
(Insert Figure 4.4 — Simplified Workflow) ]
2 / 20

## Slide 4
Uncertainty Modeling: Type-1 (T1FS) vs Interval Type-2 (IT2FS)
Type-1 Fuzzy Set (T1FS)
(Zadeh [6], 1965)
Membership grade: precise number ∈ [0,1]
Suitable for simple linguistic uncertainty
Cannot model uncertainty in the membership function itself
Limitation: assumes membership perfectly known
Interval Type-2 Fuzzy Set (IT2FS)
(Mendel & John [8])
Membership grade: interval — models higher-order uncertainty
Bounded by Upper MF (UMF) and Lower MF (LMF)
Footprint of Uncertainty (FOU) = area between UMF & LMF
Captures expert disagreement, noise, incomplete data
Key Insight: IT2FS has a second layer of uncertainty — uncertainty about the membership function itself. This is critical for real-world transportation.
3 / 20

## Slide 5
Research Gaps & Problem Statement
Gap 1
No comparative study of MVAM vs MRAM under IT2 uncertainty
Gap 2
Pratihar et al. [14] introduced MVAM — but no alternative heuristic tested
Gap 3
No systematic benchmarking across multiple scales
Gap 4
Transportation problem structure not studied as performance predictor
Gap 5
FOU sensitivity not analyzed in IT2 transportation literature
Gap 6
No balance-restoration mechanism after KM defuzzification
→ This thesis fills all six gaps by building a complete IT2-TrFTP pipeline and comparing MVAM vs MRAM at scale.
4 / 20

## Slide 6
Research Objectives & Scope
Research Objectives
1.
Develop an IT2 trapezoidal fuzzification pipeline
2.
Implement KM type-reduction & defuzzification
3.
Design a balance-preserving normalization layer
4.
Compare MVAM vs MRAM under IT2 uncertainty
5.
Benchmark across multiple problem scales
6.
Conduct Cost Magnitude & FOU Sensitivity Analysis
Scope
Included:
✓ Balanced TP only
✓ IT2 trapezoidal fuzzy
✓ MVAM & MRAM (IBFS)
✓ MODI (optimization)
✓ Synthetic datasets
✓ Cost & FOU sensitivity
Excluded:
5 / 20

## Slide 7
IT2-TrFTP Framework: Three-Dimensional Fuzzification
Geometric Uncertainty
Symbol: αg
Controls UMF spread/shape
Wider αg → wider trapezoid
Models spatial ambiguity
Epistemic Uncertainty
Symbol: ρ
Controls LMF contraction
ρ close to 1 → narrow FOU
Models knowledge gap
Confidence/Variability
Symbol: γ
Controls LMF height
Models membership certainty
Orthogonal degree of freedom
UMF Trapezoid Construction:
Ã_UMF = (a, b, c, d) where:
a = x·(1 − αg) b = x·(1 − αg/2) c = x·(1 + αg/2) d = x·(1 + αg)
x = crisp parameter αg = geometric uncertainty coefficient
[ Figure 3.3: IT2FS with FOU
(Insert from Thesis — UMF/LMF trapezoid diagram) ]
Fuzzification applies to: (1) Transportation Costs cᵢⱼ | (2) Supply Values sᵢ | (3) Demand Values dⱼ
6 / 20

## Slide 8
KM Type-Reduction & Centroid Defuzzification
Step 1: Type-Reduction
Karnik–Mendel (KM) Algorithm [9][10]
Computes centroid interval [y_l, y_r]
Iterative switch-point procedure — guaranteed convergence
Step 2: Centroid Formula
y_l = left centroid
y_r = right centroid
(computed separately)
Step 3: Defuzzification
y* = (y_l + y_r) / 2
y* = crisp scalar value
Used as input to transportation algorithms
Centroid Type-Reduction (KM):
C(Ã) = [y_l, y_r]
y_l = left endpoint of centroid interval
y_r = right endpoint of centroid interval
Ã = IT2 trapezoidal fuzzy number
Crisp Output:
y* = (y_l + y_r) / 2
[ Figure 3.4 / 3.5: KM Algorithm Flowchart (Insert from Thesis) ]
N = 1000 discretization points | Convergence tolerance = 10⁻⁸ | Applied to every cost, supply & demand IT2 parameter
7 / 20

## Slide 9
Balance-Preserving Normalization Layer (Novel Contribution)
The Problem: Post-Defuzzification Imbalance
Supply & demand fuzzified independently
→ KM centroids diverge slightly
→ Σsᵢ ≠ Σdⱼ after defuzzification
→ Transportation problem becomes infeasible!
The Solution: Proportional Normalization
Compute anchor: T = (Σs_KM + Σd_KM) / 2
Scale demand: dⱼ* = dⱼ · (T / Σdⱼ)
Result: Σsᵢ = Σdⱼ* exactly
Normalization Formula:
dⱼ* = dⱼ · ( T / Σⱼ dⱼ ) where T = ( Σᵢ sᵢ_KM + Σⱼ dⱼ_KM ) / 2
dⱼ = raw defuzzified demand | T = symmetric anchor | Result: exact balance Σsᵢ = Σdⱼ*
4 Mathematical Guarantees:
✓
Exact balance restoration — Σsᵢ = Σdⱼ always
✓
Ratio preservation — Proportional structure kept
✓
Full determinism — No randomness
✓
Minimal distortion — Correction < 0.02% per element
8 / 20

## Slide 10
MVAM — Modified Vogel's Approximation Method
Algorithm Steps:
1
Compute row penalty: Pᵢ = c_i(1) − c_i(2)
2
Compute column penalty: Pⱼ = c_j(1) − c_j(2)
3
Select row/column with largest penalty
4
Allocate max to minimum-cost cell in that row/col
5
Update supply & demand; remove exhausted row/col
6
Repeat until all supplies & demands are satisfied
Pᵢ = c_i(1) − c_i(2) where c_i(1) = min cost in row i, c_i(2) = 2nd min cost in row i
When MVAM Excels:
✓ Wide cost range (cₘₐₓ − cₘᵢₙ large)
✓ Low noise in cost matrix
✓ Penalty-Sharp regime: clear differentiation
When MVAM Struggles:
✗ Narrow cost range
✗ High noise (penalties become indistinguishable)
✗ Penalty-Diffuse regime
[ Operates on defuzzified crisp cost matrix C* from KM pipeline ]
9 / 20

## Slide 11
MRAM — Modified Russell's Approximation Method
Algorithm Steps:
1
Compute row reference value: uᵢ = max_j (cᵢⱼ) for each row i
2
Compute col reference value: vⱼ = max_i (cᵢⱼ) for each col j
3
Compute Russell measure: Rᵢⱼ = cᵢⱼ − uᵢ − vⱼ
4
Select cell with most negative Rᵢⱼ (highest opportunity)
5
Allocate max to that cell; update supply & demand
6
Repeat until all allocations satisfied
Rᵢⱼ = cᵢⱼ − uᵢ − vⱼ where uᵢ = max row cost, vⱼ = max col cost
Key Difference from MVAM:
MVAM uses local penalty (row/col min diff)
MRAM uses global cost structure (max references)
MRAM estimates opportunity cost relative to entire row/col landscape
When MRAM Excels:
✓ Narrow cost range (homogeneous matrix)
✓ High noise (penalty signals weak)
✓ Penalty-Diffuse regime
✓ Global topology still informative
[ Figure 4.1: RAM Allocation Flowchart (Insert from Thesis) ]
10 / 20

## Slide 12
MODI Optimization & Performance Evaluation Metrics
Modified Distribution Method (MODI) [5][13]
Dual variables for occupied cells:
uᵢ + vⱼ = cᵢⱼ for all basic cells
uᵢ = row potential vⱼ = col potential cᵢⱼ = cost of basic cell
Opportunity cost for non-basic cells:
Δᵢⱼ = cᵢⱼ − uᵢ − vⱼ
Δᵢⱼ = opportunity cost If all Δᵢⱼ ≥ 0: OPTIMAL
If any Δᵢⱼ < 0: loop-shift to reduce cost. Repeat until optimal.
Performance Metrics
IBFS Cost
Z_IBFS = Σᵢ Σⱼ cᵢⱼ · xᵢⱼ⁽⁰⁾
MODI Cost
Z_OPT = Σᵢ Σⱼ cᵢⱼ · xᵢⱼ*
% Improvement
Δ% = (Z_IBFS − Z_OPT)/Z_IBFS × 100
Runtime T
30 repetitions, 95% CI (t-dist.)
MODI Iterations
Count until Δᵢⱼ ≥ 0
Both MVAM and MRAM are followed by the SAME MODI optimizer → isolates initialization quality from final cost comparison
11 / 20

## Slide 13
Structural Regimes: Penalty-Sharp vs Penalty-Diffuse
Penalty-Sharp Regime
MVAM Favored
Conditions:
Wide cost range: cₘᵢₙ=1, cₘₐₓ=40
Low noise: σ ≤ 0.5
Strong cost differentiation
Penalty signals clearly distinct
Instances: 40×60, 90×90, 110×110, 150×150, 200×180
Penalty-Diffuse Regime
MRAM Favored
Conditions:
Narrow cost range: cₘᵢₙ=10, cₘₐₓ=16
High noise: σ ≥ 2.0
Column-cluster structure
Penalty signals nearly equal
Instances: 60×60, 100×100, 120×120, 200×200
Parity Zone
Statistical Tie
Conditions:
Moderate cost range & noise
No strong cluster bias
Both methods converge similarly
No structural advantage exists
Instances: 3×4, 6×8, 150×150 (borderline)
100% Predictive Accuracy on all 9 non-parity instances — Structure, not size, determines the winner.
12 / 20

## Slide 14
Synthetic Dataset Design & Experimental Protocol
Why Synthetic Datasets?
No public IT2 fuzzy TP benchmark exists
Small instances only in Pratihar et al. [14]
Need to isolate structural regime effects
Fully reproducible via fixed seeds (NumPy PCG64)
Dataset Inventory
Small
3×4, 6×8
Medium
40×60, 60×60, 90×90
Large
90×90, 100×100, 110×110, 120×120
Extended
150×150, 200×180, 200×200
Generation Parameters:
Parameter
Small
Medium
Large
Supply/Demand Range
(5,15)
(50,120)
(80,200)
Cost Range (Sharp)
(1,40)
(1,40)
(1,40)
Cost Range (Diffuse)
(10,16)
(10,16)
(10,16)
Noise Level
σ=0.5
σ=2.0
σ=5.0
Benchmarking Protocol
30 repetitions per (instance, method) pair
95% CI using Student's t-distribution (ν=29)
CV < 10% required for valid measurement
timer: Python time.perf_counter()
JSON datasets — seed-controlled, fully reproducible
13 / 20

## Slide 15
Results: Small & Medium Scale (3×4 and 40×60 / 60×60)
3×4 Instance (Parity Zone | Pratihar et al. [14])
MVAM
MRAM
IBFS Cost
69.1461
67.0683 ✓
MODI Cost
67.0683
67.0683
MODI Iters
3
1 ✓
Regime
Parity
-
Both converge to identical optimal cost.
RAM uses 1 MODI iteration vs VAM's 3.
Source: Table 6.2
40×60 — Penalty-Sharp (VAM wins)
IBFS Cost
2,776,524 ✓
3,487,971
MODI Iters
77 ✓
161
MODI Cost
1,452,634
1,452,634
Pipeline
1.75× faster ✓
—
60×60 — Penalty-Diffuse (RAM wins)
IBFS Cost
40,943 ✗
29,547 ✓
MODI Iters
102
40 ✓
MODI Cost
28,983
28,983
Pipeline
—
1.48× faster ✓
40×60 vs 60×60: Same scale, opposite winners — proof that STRUCTURE, not SIZE, determines outcome.
14 / 20

## Slide 16
Results: Large & Extended Scale (90×90 to 200×200)
Instance
Regime
IBFS Winner
MODI Iters (VAM/RAM)
Pipeline Winner
Speed Ratio
90×90
Sharp
VAM
127 / 171
VAM+MODI
1.24×
100×100
Diffuse
RAM
172 / 65
RAM+MODI
1.51×
110×110
Sharp
VAM
197 / 277
VAM+MODI
1.30×
120×120
Diffuse
RAM
— / —
RAM+MODI
1.42×
150×150
Parity
Tie
77 / 137
VAM+MODI*
1.33×
200×180
Sharp
VAM
118 / 148
VAM+MODI
1.16×
200×200
Diffuse
RAM
449 / 207
RAM+MODI
1.50×
Within large scale: 90×90 (Sharp→VAM), 100×100 (Diffuse→RAM), 110×110 (Sharp→VAM) — alternating despite increasing size.
Source: Tables 6.6, 6.8, 6.10 | *VAM faster despite parity due to simpler internals
15 / 20

## Slide 17
Statistical Benchmarking Summary — All 11 Instances
F1
Structural Determinism of IBFS
VAM wins all 5 sharp instances
RAM wins all 4 diffuse instances
100% structural prediction rate
F2
MODI Equalizes Final Cost
7 of 11 instances: identical post-MODI cost
Remaining 4: difference < 0.20 units
(<0.003% relative difference)
F3
Pipeline Speed Follows MODI Iters
Dominant cost = MODI refinement
VAM: 1.05–1.18× faster at IBFS only
MODI overhead reverses advantage
F4
Scale Amplifies, Not Determines
200×200: largest gaps observed
But direction determined by structure
3 consecutive large sizes → alternating winner
F5
Statistical Reliability Increases
3×4: CV > 50% (noise dominated)
6×8: CV < 10% (reproducible)
60×60+: CV < 4% (highly reliable)
F6
No Universal Winner
VAM+MODI faster: 6 instances
RAM+MODI faster: 4 instances
N/S tie: 1 instance (3×4)
[ Figure 6.1: Complete Timing Benchmark Summary (Insert from Thesis) ]
16 / 20

## Slide 18
Problem Structure vs Problem Size as Performance Determinant
Central Thesis Hypothesis: Transportation problem structure (penalty topology) is a STRONGER predictor than problem size.
Observation 1
Within-Group Size Alternation
90×90 → VAM wins (Sharp)
100×100 → RAM wins (Diffuse)
110×110 → VAM wins (Sharp)
Same scale class, 3 different structural regimes → 3 different winners
Observation 2
Cross-Group Structure Consistency
All Sharp instances (any size) → VAM wins
All Diffuse instances (any size) → RAM wins
Structure predicts direction at EVERY scale
Observation 3
Scale Modulates Magnitude
200×200 penalty-diffuse: VAM gap = 15.1%
(larger than 60×60 gap of 28.2%)
Penalty diffuseness compounds with size
but DIRECTION is always structure-determined
Conclusion: Structural classification (penalty-sharp / penalty-diffuse) achieves 100% predictive accuracy on 9 non-parity instances.
17 / 20

## Slide 19
Cost Magnitude Sensitivity Analysis
Perturbation Design:
All UMF & LMF vertices scaled by M ∈ {0.80, 0.90, 1.10, 1.20}
FOU gap ratios preserved (uncertainty structure unchanged)
KM type-reduction re-run on each perturbed dataset
Supply & demand unchanged
Perturbation Levels (Table 7.1):
C1 ×0.80 — −20% (cost reduction)
C2 ×0.90 — −10%
Baseline ×1.00 — Baseline (Chapter 6)
C3 ×1.10 — +10%
C4 ×1.20 — +20% (cost increase)
3×4 (Parity)
→ RAM IBFS superior in all 5 scenarios
→ Both converge to same MODI cost
→ VAM improvement % = 3.00% (exact constant)
40×60 (Sharp)
→ VAM IBFS superior in all 5 scenarios
→ VAM+MODI 1.69–1.86× faster
→ Final costs within 0.003%
100×100 (Diffuse)
→ RAM IBFS superior in all 5 scenarios
→ RAM+MODI 1.52–1.71× faster
→ RAM improvement ≈ 1.01–1.02%
Key Finding: IBFS ranking, pipeline speed, and final cost equality — ALL stable across ±20% cost perturbation.
18 / 20

## Slide 20
Footprint of Uncertainty (FOU) Sensitivity Analysis
FOU Perturbation Design:
Gap quantities: G1 = b₁−a₁ G2 = b₂−a₂
G3 = a₃−b₃ G4 = a₄−b₄
New LMF: b₁ᴺ = a₁ + G1×M (and similarly for b₂,b₃,b₄)
M<1 → narrow FOU M>1 → wide FOU
FOU Perturbation Levels (Table 7.8):
F1 ×0.80 — FOU narrows by 20%
F2 ×0.90 — FOU narrows by 10%
Baseline ×1.00 — Baseline
F3 ×1.10 — FOU widens by 10%
F4 ×1.20 — FOU widens by 20%
3×4
→ RAM IBFS superior in all FOU scenarios
→ VAM improvement ≈ 3.00% (stable)
→ Wider FOU → slight cost decrease (KM centroid effect)
40×60
→ VAM IBFS advantage maintained
→ VAM+MODI 1.69–1.87× faster
→ MODI costs within 0.002%
100×100
→ RAM IBFS advantage maintained
→ RAM+MODI 1.60–1.65× faster
→ Monotone cost decrease as FOU widens
FOU Effect: Wider FOU → slightly lower defuzzified costs (KM centroid shifts). Does NOT change algorithm rankings.
[ Figure 7.11: Complete Sensitivity Analysis Overview (Insert from Thesis) ]
19 / 20

## Slide 21
Joint Robustness Assessment — 24 Perturbation Experiments
0 Ranking Reversals
across 24 independent perturbation experiments (3 scales × 2 types × 4 levels)
Robustness Map — IBFS Winner by Scenario (all identical = stable):
3×4
Cost -20
Winner: RAM
3×4
Cost -10
Winner: RAM
3×4
Cost +10
Winner: RAM
3×4
Cost +20
Winner: RAM
40×60
Cost -20
Winner: VAM
40×60
Cost -10
Winner: VAM
40×60
Cost +10
Winner: VAM
40×60
Cost +20
Winner: VAM
100×100
FOU -20
Winner: RAM
100×100
FOU -10
Winner: RAM
100×100
FOU +10
Winner: RAM
100×100
FOU +20
Winner: RAM
S1: Perfect ranking stability under cost perturbation
S2: Perfect ranking stability under FOU perturbation
S3: MODI final cost equal across all scenarios
S4: Improvement rate invariance (LP basis invariance theorem)
S5: FOU perturbation produces monotone cost shifts only
S6: Structural classification is perturbation-invariant
20 / 20

## Slide 22
Contributions, Limitations & Future Research Directions
C1
Complete IT2-TrFTP Pipeline
First end-to-end: 3D fuzzification + KM + normalization + dual IBFS + MODI
C2
Structural Classification
Penalty-sharp / Penalty-diffuse framework — 100% predictive accuracy on non-parity instances
C3
Balance-Enforcement Layer
Novel normalization restoring Σsᵢ = Σdⱼ after asymmetric KM defuzzification
C4
2D Sensitivity Analysis
Cost + FOU robustness — new result: FOU does not cause ranking reversals
Limitations
• Synthetic datasets only — no real-world validation
• Only MVAM vs MRAM compared (other heuristics excluded)
• Fuzzification parameters (δ, α, β, γ) not varied systematically
Future Research Directions
→ Pre-computation structural diagnostic (CV-based)
→ Replace KM with Nie–Tan [44] approximation at large scale
→ Validate on real logistics datasets
→ Extend to multi-objective IT2-TrFTP
Algorithm performance is structurally determined — understanding cost topology is the key to principled deployment decisions.
20 / 20

## Slide 23
BANGLADESH UNIVERSITY OF ENGINEERING AND TECHNOLOGY
Thank You
Comparative Performance and Robustness Analysis of
Modified Vogel's and Modified Russell's Approximation Methods
under Interval Type-2 Trapezoidal Fuzzy Uncertainty
Md Sadiqul Haque (2008082) | Md Tanjil Haque (2008094)
Supervisor: Dr. Kais Bin Zaman, Professor, IPE, BUET | June 2026
Questions & Discussion Welcome